## Slide 1: Three Challenges to Reliable Data Transport over Heterogeneous Wireless Networks
Hari Balakrishnan
Daedalus Group
Department of Electrical Engineering and Computer Science
University of California at Berkeley
http://daedalus.cs.berkeley.edu
http://www.cs.berkeley.edu/~hari

## Slide 2: Protocol Design for the Internet
Internet invariants
  Heterogeneity
  Large scale
Adaptation is crucial
  Protocols
  Applications
Importance of incremental deployment
To design and implement adaptive protocols
and applications for the Internet

## Slide 3: Motivation
But wireless data is floundering...
  Enormous heterogeneity
  Poor performance
Goal: To make wireless devices first-class Internet citizens
Year
# of units/hosts
(millions)
Sources:
Ericsson, Inc.
Matthew Gray, MIT
Cellular phones
Internet
hosts
Rapid growth

## Slide 4: Wireless Heterogeneity
In-Building
Campus-Area
Packet Radio
Metro-Area
Regional-Area
Cellular Digital
Packet Data (CDPD)
Metricom Ricochet
Lucent WaveLAN
IBM Infrared

## Slide 5: Wireless Performance
Goal: To bridge the gap between perceived and rated performance

## Slide 6: Methodology
Simulation (UCB/LBNL/VINT ns network simulator with several enhancements)
Design solutions
Evaluate solutions in simulation
Deploy real networks
Measure performance
Identify and analyze problems
Implement best solutions on real networks
Evaluate performance

## Slide 7: Structure
TCP Background
Challenge #1: wireless bit-errors
  Solution: Berkeley Snoop Protocol
Challenge #2: asymmetry and latency variation
  Solution: TCP mods + link-level schemes
Challenge #3: low channel bandwidths
  Solution: Enhanced TCP loss recovery
Conclusions

## Slide 8: Cellular Network Topology
Base Station (BS)
Fixed Host (FH)
Wireless Cell
Internet
Mobile Host (MH)

## Slide 9: Internet Service Model
Need reliable data transport protocols
  Web, file transfer, remote terminal, e-mail,...
Functions
  Efficient loss recovery
  Robust congestion and flow control
Internet
A best-effort network: losses & reordering can occur
Router

## Slide 10: Transmission Control Protocol (TCP)
Internet standard for reliable transport
  95% of all bytes, 90% of all packets (Thompson, et al.)
Flexible protocol framework
  New algorithms within this protocol framework
  Incremental deployment of modifications
7
4
3
6
5
Cumulative Acknowledgments (ACK)
1
2
3
4
2

## Slide 11: TCP Overview
0
  Window-based algorithm to determine sustainable rate
  Upon congestion, reduce window
  “ACK clocking” sends data smoothly
8
1
1
7
6
1
3
4
1
2
lost
1
5
Timeouts based on mean round-trip time (RTT) and deviation
Fast retransmissions based on duplicate ACKs
1. Loss recovery
2. Congestion control [Jacobson88]
0
10
9

## Slide 12: TCP Dynamics
Data
ACKs
Window
Fast retransmission
Duplicate ACKs
Sequence number (bytes)
Time (s)
RTT

## Slide 13: Wireless Transport: The Three Challenges
Preponderance of wireless bit-errors
  Corruption vs. congestion losses
Asymmetric effects
  Bandwidth asymmetry
  Latency variability
Low channel bandwidths
  Small windows

## Slide 14: Challenge #1: Wireless Bit-Errors
Internet
Router
Loss  Congestion
2
3
2
1
Loss ==> Congestion
2
1
0
Burst losses lead to coarse-grained timeouts
Result: Low throughput [CI95]

## Slide 15: Performance Degradation
Time (s)
Sequence number (bytes)
TCP Reno
(280 Kbps)
Best possible
TCP with no errors
(1.30 Mbps)
2 MB wide-area TCP transfer over 2 Mbps Lucent WaveLAN

## Slide 16: Conventional Approaches
Link-layer protocols [LC83]
End-to-end
ARQ/FEC
Adverse interactions with transport layer
  Timer interactions [DCY93]
  Interactions with fast retransmissions
  Large end-to-end round-trip time variation
Wired connection
Wireless connection
Split connections [YB94,BB95]
  Wireless connection need not be TCP
Hard state at base station
  Complicates mobility
  Vulnerable to failures
Violates end-to-end semantics
Base Station

## Slide 17: Our Solution: Berkeley Snoop Protocol
Shield TCP sender from wireless vagaries
  Eliminate adverse interactions between protocol layers
  Congestion control only when congestion occurs
The End-to-End Argument [SRC84]
  Preserve TCP/IP service model: end-to-end semantics
  Is connection splitting fundamentally important?
Eliminate non-TCP protocol messages
  Is link-layer messaging fundamentally important?
Fixed to mobile: transport-aware link protocol
Mobile to fixed: link-aware transport protocol

## Slide 18: Snoop Protocol: FH to MH
FH Sender
Mobile Host
Base Station
5
1
1
2
3
4
6
Snoop agent: active interposition agent
  Snoops on TCP segments and ACKs
  Detects losses by duplicate ACKs and timers
  Suppresses duplicate ACKs from FH sender
Cross-layer protocol design: snoop agent state is soft
Snoop agent

## Slide 19: Snoop Protocol: FH to MH
Mobile Host
1
Base Station
Snoop Agent
FH Sender

## Slide 20: Snoop Protocol: FH to MH
Mobile Host
1
2
3
4
Base Station
5
FH Sender

## Slide 21: Snoop Protocol: FH to MH
Mobile Host
Base Station
5
1
1
2
3
4
6
FH Sender

## Slide 22: Snoop Protocol: FH to MH
Mobile Host
5
1
2
3
4
Base Station
3
2
6
2
1
Sender

## Slide 23: Snoop Protocol: FH to MH
Mobile Host
6
1
2
3
4
Base Station
4
3
1
5
2
ack 0
Sender
Duplicate ACK

## Slide 24: Snoop Protocol: FH to MH
Mobile Host
1
2
3
4
Base Station
1
1
5
6
4
3
2
Sender
Retransmit from cache
at higher priority
ack 0
ack 0
ack 0
6
5

## Slide 25: Snoop Protocol: FH to MH
Mobile Host
1
2
3
4
Base Station
1
1
Suppress
Duplicate Acks
5
6
4
3
2
Sender
5
ack 0
ack 4

## Slide 26: Snoop Protocol: FH to MH
Base Station
6
5
6
1
4
3
2
5
Sender
ack 4
ack 5
Clean cache on new ACK

## Slide 27: Snoop Protocol: FH to MH
Mobile Host
Base Station
6
5
4
3
2
1
Sender
ack 4
6
ack 6
ack 5

## Slide 28: Snoop Protocol: FH to MH
Mobile Host
Base Station
5
4
3
2
1
Active soft state agent at base station
Transport-aware reliable link protocol
Preserves end-to-end semantics
6
Sender
ack 5
ack 6
7
8
9

## Slide 29: Handling Mobility
Home Agent
Sender
Base Station
(Snoop agent)
Base Station
(Snoop agent)
5
4
3
2
1
2
1
1

## Slide 30: Handling Mobility
Home Agent
Sender
Base Station
(Snoop agent)
Base Station
(Snoop agent)
6
5
4
1
3
1
1
3
2
2

## Slide 31: Snoop Protocol: MH to FH
Receiver
Base Station
Sender
2
3
2
1
0
Caching and retransmission will not work
  Losses occur before packet reaches BS
  Congestion losses should not be hidden
Solution: Explicit Loss Notifications (ELN)
  In-band message to TCP sender
  General solution framework

## Slide 32: Snoop Protocol: MH to FH
Base Station
1
Sender
0
Receiver

## Slide 33: Snoop Protocol: MH to FH
Base Station
Sender
2
3
2
1
Receiver
0

## Slide 34: Snoop Protocol: MH to FH
Base Station
1
2
Sender
1
4
5
3
ack 0
Receiver
0
Add 1 to list of holes after checking for congestion

## Slide 35: Snoop Protocol: MH to FH
Base Station
1
ack 0
3
4
Sender
1
ack 0
ack 0
5
6
Receiver
2
0
Duplicate ACKs

## Slide 36: Snoop Protocol: MH to FH
Base Station
1
6
Sender
1
ack 0
ack 0
ack 0
ack 0
ack 0
ELN information
on duplicate ACKs
3
Receiver
2
0
5
4
ELN marking

## Slide 37: Snoop Protocol: MH to FH
Base Station
1
Sender
1
ack 0
ack 0
ack 0
ack 0
ELN information
on duplicate ACKs
1
Retransmit on dup ACK + ELN
No congestion control now
ack 0
3
Receiver
2
0
5
4
6

## Slide 38: Snoop Protocol: MH to FH
Base Station
Sender
Link-aware transport decouples congestion control from loss recovery
Technique generalizes nicely to wireless transit links
3
Receiver
2
0
5
4
6
ack 6
1
Clean holes on new ACK

## Slide 39: End-to-End Enhancements
Selective ACKS (SACK) for burst losses [FF96,KM96,MMFR96,B96]
Snoop protocol: no changes to fixed hosts on the Internet
ack 0 [sack 2]
ack 0 [sack 2,4]
Selective ACKs
0
2
4
ELN to decouple congestion from loss recovery

## Slide 40: Snoop Performance Improvement
Best
possible
TCP
(1.30
Mbps)
Time (s)
Time (s)
Sequence number (bytes)
Snoop (1.11 Mbps)
TCP Reno
(280 Kbps)
2 MB wide-area TCP transfer over 2 Mbps Lucent WaveLAN

## Slide 41: Performance: FH to MH
TCP Reno
SPLIT
TCP SACK
SPLIT-SACK
Snoop
Snoop+SACK
1/Bit-error Rate (1 error every x Kbits)
Throughput (Mbps)
Snoop+SACK and Snoop perform best
Connection splitting not essential
TCP SACK performance disappointing
Typical error rates
2 MB local-area TCP transfer over 2 Mbps Lucent WaveLAN

## Slide 42: Empirical Error Models
Duration (ln ms)
Error-free duration
Error duration
Data collected from Reinas Env. Monitoring Network Santa Cruz, CA
CDF

## Slide 43: Real-World Web Performance
# of downloads in 1000 s
Empirical Web workload
model from real traces
[Mah97]
Empirical wireless error
model from real traces
of Reinas wireless network,
UC Santa Cruz
Snoop performance improvement: 3X-6X over Reno & SACK

## Slide 44: Benefits of TCP-Awareness
30-35% improvement for Snoop: LL congestion window is small (but no coarse timeouts occur)
Connection bandwidth-delay product = 25 KB
0
0
10
20
30
40
50
60
70
80
20000
30000
40000
50000
60000
10000
Time (sec)
Congestion Window (bytes)
LL (no duplicate ack suppression)
Snoop
Suppressing duplicate acknowledgments and TCP-awareness
leads to better utilization of link bandwidth and performance

## Slide 45: Split-Connection Congestion Window
0
10000
20000
30000
40000
50000
60000
0
20
40
60
80
100
120
Time (sec)
Congestion Window (bytes)
Wired connection does not shrink congestion window
but
wireless connection times out often, causing sender to stall
Wired connection
Wireless connection

## Slide 46: Snoop Protocol Status
BSD/OS implementation
  Integrated with Daedalus handoff software [SBK97]
Version 1 released 1996; Version 2 in beta
Daily production use at Berkeley and UC Santa Cruz
Several hundred downloads
  Ports to Linux, FreeBSD, NetBSD
Papers: MOBICOM 95, SIGCOMM 96, Trans. on Networking (Dec. 97)

## Slide 47: Summary: Wireless Bit-Errors
Problem: wireless corruption mistaken for congestion
Solution: Berkeley Snoop Protocol
General lessons
  Lightweight soft-state agent in network infrastructure
    Guided by the End-to-End Argument
    Fully conforms to the IP service model
  Cross-layer protocol design & optimizations
Transport
Network
Link
Physical
Link-aware transport (ELN)
Transport-aware link (Snoop agent at BS)

## Slide 48: Challenge #2: Asymmetric Effects
Asymmetric access technologies
  ADSL, (wireless) cable modems, DBS, etc.
  Low-bandwidth ACK channel [LM97, KVR98]
Packet radio networks
  Metricom’s Ricochet, CDPD, etc.
  Adverse interactions between data and ACK flow
Problem: Imperfect ACK feedback degrades TCP performance

## Slide 49: The Character of Asymmetry
Bandwidth: 10-1000 times more in the forward direction
Latency: Variability due to MAC protocol interactions
Packet loss: Higher loss- or error-rate in one direction
The network and traffic characteristics in one
direction significantly affect performance in the other
Server
Client
Forward
ACK
Router
Router

## Slide 50: Bandwidth Asymmetry Problems
Server
Client
Forward
ACK
Router
Bottleneck Router
0
Data 8
Data 11
Data 10
Data 9
3
2
1
4
5
6
7
1. Acks arrive slowly (large buffer)
2
5
4
7
1
3
6
2. Acks are dropped (small buffer)
1
Data
Data
3. Acks are queued behind data packets
Ack flow
Lakshman & Madhow 97
Kalampoukas et al. 97
Balakrishnan et al. 97

## Slide 51: Hybrid Wireless Cable Measurements
0
1
2
3
4
5
6
0
20
40
60
80
100
120
140
160
180
200
TCP Throughput (Mbps)
10 Mbps Ethernet
28.8 C-SLIP
28.8 SLIP
9.6 C-SLIP
9.6 SLIP
Socket Buffer Size (KB)
Return channel speed and latency affects performance

## Slide 52: Latency Asymmetry: Packet Radio Networks
Internet
PT
ER
FH
GW
MH
Modem PR
ER
ER
PT
PT
PT
PT
PT
PT
Fixed Host
Ethernet Radios
Poletop Radios
Mobile Host
RTS
CTS
Half-duplex radios
Synchronization before communication

## Slide 53: Packet Radio Networks
Data
Internet
PT
ER
FH
GW
MH
Modem PR
ER
ER
PT
PT
PT
PT
PT
PT
Fixed Host
Ethernet Radios
Poletop Radios
Mobile Host
Data
Ack
RTS
No response
Exponential
backoff
Problem: Large and variable communication latency

## Slide 54: Problem: Large Round-Trip Time Variations
Example: Metricom Ricochet Wireless Network
Mean rtt = 2.45s, std deviation = 1.5s  long timeout!
Long idle periods after multiple losses (~ 20 Kbps)
In contrast, UDP throughput = 50-64 Kbps
ACK flow affects data latency
Fast retransmissions
Timeouts

## Slide 55: Solutions
Problems arise because of imperfections in the ACK feedback
Reduce frequency of acks
  ACK Filtering (AF)
  ACK Congestion Control (ACC)
Handle infrequent acks
  Sender Adaptation (SA)
  ACK Reconstruction (AR)
General solution approach for asymmetric situations

## Slide 56: ACK Filtering (AF)
9
7
5
11
13
3
7
5
Forward
Router
1
Server
Client
Router
Purge all redundant, cumulative ACKs from constrained reverse queue
Used in conjunction with sender adaptation or ACK reconstruction

## Slide 57: ACK Congestion Control (ACC)
Server
Client
Router
8
Data 21
Data 22
Data 20
18
16
14
Data 19
10
Delack factor = 2
Adaptive extension of TCP delayed ACKs based on congestion feedback from router or sender
Forward

## Slide 58: ACK Congestion Control (ACC)
Server
Router
Data
Data
Data
22
Data
12
Data
RED [FJ93] marking
of ECN bit [F94]
(Explicit Congestion
Notification)
Delack factor = 2
Client
Forward

## Slide 59: ACK Congestion Control (ACC)
Router
Data
Data 40
Data
Data
22
Echo ECN marking
to receiver
Delack factor = 2
Forward
Server
Client

## Slide 60: ACK Congestion Control (ACC)
Router
Data 42
Data 43
Data 41
36
40
Data 40
Delack factor = 4
Forward
Server
Client

## Slide 61: Sender Adaptation (SA)
Infrequent ACKs cause slow window growth
Sender tends to be bursty
Server
1
9
15
1. cwnd += 8
cwnd += 8/cwnd
Increment window by amount of data ack’d
19
20
21
22
. . .
2.
Regulation: pace packets out at rate estimated by cwnd/srtt
This reduces burstiness
Router
Forward
Client

## Slide 62: ACK Reconstruction (AR)
9
7
5
1
11
13
3
7
5
ACK filter
ACK reconstructor
7
5
3
9
Server
Forward
Client
Regenerates ACKs at other end of reverse channel
Shields sender from large gaps in ack sequence
AR rate determined by
  input ACK rate
  target ACK spacing
1

## Slide 63: Bandwidth Asymmetry Performance
  TCP transfers in the forward direction alone
  Maximum window size 100 KB; no losses on forward path
  Header compression helps
  Large reverse channel buffer hurts for Reno and ACC
  Fairness greatly improves using AF and ACC for multiple transfers

## Slide 64: Multihop Wireless Simulations
  1 to 3 wireless hops on path
  Radio turnaround time = 3-12 ms
  Radio queue size = 10 packets
  Exponential backoff in multiples of 20 ms slots
ER
PT
Client
Server
100 Kbps,
10 ms
10 Mbps
1 ms
PT
PT

## Slide 65: Performance: Single Transfer
AF reduces chances that peer radio is busy
  MAC backoffs less frequent
Round-trip std deviation reduces from 1.5 s to 0.6 s
Throughput (Kbps)
AF: 20-35% throughput improvement compared to Reno

## Slide 66: Performance: Concurrent Transfers
Metrics: utilization and fairness [Jain90]
Simultaneous connections over 2-hop network
  Performance more predictable and consistent with AF
Unpredictable performance caused by long timeouts
AF: 25% improvement in fairness over Reno

## Slide 67: Combining Technologies
Internet
server
Internet
Hybrid PoP
Client
10 Mbps, 2 ms
Wireless
transmitter
PT
ER
Requests & acks
Web data
Wireless cable forward channel with packet radio reverse channel
Workload: Multiple concurrent Web-like transfers
Issues: both bandwidth and latency asymmetries
Main result: Ack filtering tremendously improves scaling behavior (average completion time vs. # of concurrent transactions)

## Slide 68: Summary: Asymmetric Effects
General definition of asymmetry
  Problem: ACK channel impacts TCP performance
Classification of types of asymmetry
  Bandwidth asymmetry due to technologies
  Latency asymmetry due to MAC interactions
General solutions: Two-pronged approach
  Reduce frequency of ACKs (AF, ACC)
  Handle infrequent ACKs (SA, AR)
Status
  BSD/OS 3.0 implementation
  Papers: MOBICOM 97, ACM Mobile Networks 98

## Slide 69: Challenge #3: Low Bandwidth
Sender
Receiver
3
2
1
4
Small transmission window size
  Timeouts for most losses
Result: Unacceptably low throughput
Low channel bandwidths
Burst packet losses
Short Web transfers

## Slide 70: Enhanced TCP Loss Recovery
Sender
Receiver
1
Goal: Better data-driven loss recovery
Web trace analysis: 25% of all timeouts after at least 1 packet was successfully received

## Slide 71: Enhanced TCP Loss Recovery
Sender
Receiver
3
2
ack 0
ack 0
1st dup ack
1
4
6
5
Early “fast recovery”: send new packet on dup ACK
Need to guard against packet reordering [Paxson97]
5

## Slide 72: Performance: Enhanced Recovery
Timeouts occur only on persistent congestion
  Entire window is lost
  Retransmission is lost
Time (s)
Packet sequence #
Enhanced Recovery
TCP SACK

## Slide 73: TCP Loss Recovery: Status
SACK implementation in BSD/OS
  Released March 1996 (IETF presentation); patches June 1996
  Running in Daedalus network and Web server
  222 downloads in 52 weeks
Enhanced loss recovery
  BSD/OS implementation
  Experiments over Internet paths and Ricochet network
  Papers: INFOCOM 98

## Slide 74: Summary
Three fundamental challenges to efficient reliable data transport over wireless networks
  Wireless bit-errors: Berkeley Snoop protocol (local recovery + ELN)
  Asymmetric effects: Two-pronged approach with end-to-end and link schemes (AF, ACC, SA, AR)
  Low channel bandwidths: Enhanced TCP loss recovery
Lessons for protocol design
  Cross-layer protocol optimizations: Snoop, ELN, AF
  Soft-state network agents: Snoop, AR
  Data-driven loss recovery: Snoop, Enhanced TCP loss recovery

## Slide 75: Future Directions
Transport protocols
Large-scale Networks of Devices (NOD)
Protocol framework for Internet client-server apps
Framework for evaluating and designing congestion control
Internet measurement and analysis